File	Type of file	functional forms present	units	Description
ff*.atp	atom type parameter			- atom types, masses (amu), comment / - can change or add an atom type here
ff*.itp:	include topology			- these files are “included” in topology files (*.top)
ff*bon.itp / (5.3.2) / [bondtypes] / [angletypes] / [dihedraltypes]	bonded parameters	bond and angle pot: / 1 = harmonic / 2= GROMOS-96 / dihedrals: / 1= proper / 2=improper / 3 = Ryckaert-Belleman		-parameters for bonds, bond angles, improper and proper dihedrals / - can add bonded parameters / - can include parameters for new atom types ( must add these new atom types to ff*.atp as well)
ff*nb.itp / (5.3.3) / [atomtypes]	non-bonded parameters	rule 1 = 4%epsilon_i%sigma_i^6 / rule 2, 3 4%epsilon_i%sigma_i^12 / combination of atom i, j: / if rule = 1,3 use C_ij^(6)=(C_i^(6)C_j^(6))^(1/2) and same for C_ij^(12) / else rule =2 use %sigma_ij = (1/2)(%sigma_i+%sigma_j); %epsilon_ij = sqrt[%epsilon_i%epsilon_j]	%sigma_i [nm] / %epsilon_i [kJ/mol]	-van der waals parameters c6, c12
ff*.rtp / (5.5.1)	residue topology parameter			-bonds, charge, charge groups, improper dihedral for a frequently used building block / -don't change this file / -can add protein residue to the database (must also add name to aminoacids.dat) / -must construct a builiding block in this file for the “strange residue” that is in the PDB